M-F Athletic Company	May 2019

1600 Division Road

West Warwick, RI 02893

Toll Free		(800) 556-7464

Phone		(401) 942-9363

Fax		(800) 682-6950

Web Site		www.mfathletic.com

E-Mail		mfathletic@mfathletic.com

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the Drawings. Delete all “Specifier Notes” after editing this section. Section numbers are from MasterFormat 1995 Edition, with numbers from MasterFormat 2004 Edition in parentheses. Delete version not required.

SECTION 11480 (11 66 23.43) (11 68 33.43)

Athletic Field Equipment

Specifier Notes: This section includes all M-F Athletic Company, Inc. field equipment pieces. Consult M-F Athletic Company, Inc. for assistance in editing this section for the specific application.

PART 1	GENERAL

  - SECTION INCLUDES

- Discus Cages

- Barrier Nets

- Discus/Shot Put Circles

- Shot Put Toe Boards

- Take-Off Board Systems

- Pole Vault Plant Boxes

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. List other sections with work directly related to this section.

A.	Section 02200 (31 23 00) Excavation and Fill: Prepare site for the installation of in-ground equipment and back fill when installation is complete.

- Section 03300 (03 30 00) Cast-in-Place Concrete: Pouring of concrete under and around athletic field equipment and surrounding areas.

C.	Section 02535 (32 18 23) Athletic Surfacing: Applying track surface material to the surrounding areas.

D. 	Section 02511 (32 12 16) Asphalt Paving: Applying asphalt sub-grade to the surrounding areas.

1.3	REFERENCES

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.4	DESIGN REQUIREMENTS

- Athletic Field Equipment: Locate positions and orientations of products and related fixtures on the site plan.

1.5	SUBMITTALS

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including materials, components, fabrication, finish, and installation instructions.

C.	Operation and Maintenance Manual:  Submit manufacturer's operation and maintenance manual; including operation, maintenance, adjustment, and cleaning instructions; trouble shooting guide; parts list.

1.6	QUALITY ASSURANCE

A.	Single Source Responsibility:  Provide all installed equipment from single manufacturer.

B.	Manufacturer's Qualifications:  Minimum of 5 consecutive years experience manufacturing athletic field equipment similar to that specified.

C.	Installer's Qualifications:  Contractor experienced with track & field installation, excavation, concrete work, asphalt paving, and track surfacing.

- Regulatory Requirements:  Athletic field equipment shall conform to latest rules and regulations.

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.7	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.  Keep temporary protective coverings in place.

C.	Handling:  Protect materials and finish from damage during handling and installation.

1.8	WARRANTY

A.	Provide 1-year warranty against defects in materials and workmanship, unless otherwise specified.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	M-F Athletic Company, Inc., 1600 Division Road, West Warwick, Rhode Island, 02893.  Toll Free (800) 556-7464.  Phone (401) 942-9363.  Fax (800) 682-6950.  Web Site www.mfathletic.com.  E-Mail mfathletic@mfathletic.com.

Specifier Notes: Specify one of the following two paragraphs regarding substitutions. Edit as required for the project. Coordinate with Section 01630 (01 25 13) – Product Substitution Procedures.

B.	Substitutions:  Not permitted.

C.	Substitutions:  Requests for substitutions will be considered in accordance with Section 01630 (01 25 13).

2.2	ATHLETIC FIELD EQUIPMENT

Specifier Notes: Specify the following paragraph for all discus cages. Add model number, either 7257-01 – First Place Aluminum High School Discus Cage, 7259-01 – First Place Steel High School Discus Cage or 7266-01 – First Place Collegiate Discus Cage.

A.	Discus Cages:  Model No. ___ Discus Cage.

Specifier Notes: Remove the following line if specifying the 7259-01 or 7266-01 discus cage.

- Ground Sleeves: Consists of six (6) ground sleeves, constructed of aluminum, 28 1/4” long.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7266-01 discus cage.

- Ground Sleeves: Consists of six (6) ground sleeves, constructed of galvanized steel, 28 1/4” long.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7259-01 discus cage.

- Ground Sleeves: Consists of seven (7) ground sleeves, constructed of aluminum, 36” long.

Specifier Notes: Remove the following line if specifying the 7259-01 or 7266-01 discus cage.

- Net Poles: Consists of six (6) net poles, constructed of 2.875” aluminum pipe. The net poles will be off-set and stand at least 13’ tall when installed in the ground sleeves. The net poles will have rope tie-off cleats. The top of the net poles will be capped. The net poles will have eye bolts to hang the hoisting ropes from.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7266-01 discus cage.

- Net Poles: Consists of six (6) net poles, constructed of 2.375” galvanized steel pipe. The net poles will be off-set and stand at least 13’ tall when installed in the ground sleeves. The net poles will have rope tie-off cleats. The top of the net poles will be capped. The net poles will have eye bolts to hang the hoisting ropes from.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7259-01 discus cage.

- Net Poles: Consists of seven (7) net poles, constructed of 4” aluminum pipe. The net poles will be off-set and stand at least 16’7” tall when installed in the ground sleeves. The net poles will have rope tie-off cleats. The top of the net poles will be capped. The net poles will have pulleys to hang the hoisting ropes from.

- Hoisting Rope: The rope used to hang the net from the net poles will be 3/8” braided polyester, 20’ long. Each rope will have a net clip.

Specifier Notes: Remove the following line if specifying the 7266-01 discus cage.

- Net: Constructed of 100% white nylon 6 yarn solution dyed black, 1 7/8”sq mesh, raschel knotless netting, UV stabilizer added and heat-set, 340 lb break strength, rope bound, 13’ x 58’.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7259-01 discus cage.

- Net: Constructed of 100% white nylon 6 yarn solution dyed black, 1 7/8”sq mesh, raschel knotless netting, UV stabilizer added and heat-set, 340 lb break strength, rope bound, 17’ x 70’.

Specifier Notes: Remove the following line if specifying the 7266-01 discus cage.

- Tension Arms: Consists of six (6) tensions arms, 24” long.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7259-01 discus cage.

- Tension Arms: Consists of seven (7) tensions arms, 30” long

- Warning Signs: Consists of three (3) warning signs constructed of polyethylene board 10” x 14”. The warning signs will be fastened to the outside of the net, at eye level, facing outward, at the front sides of the discus cage and at the rear of the discus cage.

- Barrier Nets:

Specifier Notes: Specify the following paragraph for all barrier nets.  Add model number, either 7258-   25 (works with 7257-01 and 7259-01 discus cage), or 7266-07 (works with 7266-01 discus cage).

Barrier Nets: Model No. ___ Barrier Net.

Specifier Notes: Remove the following line if specifying the 7266-07 barrier net.

- Barrier Net: Constructed of 100% white nylon 6 yarn solution dyed black, 1 7/8”sq mesh,               raschel knotless netting, UV stabilizer added and heat-set, 340 lb break strength, rope bound, 7’ x 63’.

Specifier Notes: Remove the following line if specifying the 7258-25 barrier net.

- Barrier Net: Constructed of 100% white nylon 6 yarn solution dyed black, 1 7/8”sq mesh,         raschel knotless netting, UV stabilizer added and heat-set, 340 lb break strength, rope bound, 7’ x 74’.

C.	Discus/Shot Put Circles:

Specifier Notes: Specify the following paragraph for all shot put/hammer circles. Add model number, either 7216-02 – First Place Web Shot/Hammer Circle or 7218-02 – First Place Aluminum Shot and Hammer Circle.

Shot Put/Hammer Circles:  Model No. ___ Shot Put/Hammer Circle.

Specifier Notes: Remove the following line if specifying the 7218-02 shot put/hammer circle.

- Circle: Consists of two halves of a circle constructed of 2 ¾” x 1/4” galvanized steel, with 1” x 1” galvanized steel angle cross-bracing. The circle shall be cast in concrete so that the throwing surface is depressed 3/4”. The circle shall have a 7' diameter.

Specifier Notes: Remove the following line if specifying the 7216-02 shot put/hammer circle.

- Circle: Consists of 1” x 3/4” x 1/4” aluminum angle that is roll bent to 42” (106.7cm) radius. Four arcs form the circle.  The circle can be cast in concrete so that the throwing surface is depressed 3/4” or installed directly on top of the concrete pad. The circle shall have a 7' diameter.

Specifier Notes: Specify the following paragraph for all discus circles. Add model number, either 7216-01 – First Place Web Discus Circle or 7218-01 – First Place Aluminum Discus Circle.

Discus Circles:  Model No. ___ Discus Circle.

Specifier Notes: Remove the following line if specifying the 7218-01 discus circle.

- Circle: Consists of two halves of a circle constructed of 2 ¾” x 1/4” galvanized steel, with 1” x 1” galvanized steel angle cross-bracing. The circle shall be cast in concrete so that the throwing surface is depressed 3/4”. The circle shall have an 8'-2 1/2” diameter.

Specifier Notes: Remove the following line if specifying the 7216-01 discus circle.

- Circle: Consists of 1” x 3/4” x 1/4” aluminum angle that is roll bent to 49 7/32” (125.0 cm) radius. Four arcs form the circle.  The circle can be cast in concrete so that the throwing surface is depressed 3/4” or installed directly on top of the concrete pad. The circle shall have an 8'-2 1/2” diameter.

D.	Shot Put Toe Boards:

Specifier Notes: Specify the following paragraph for all shot put toe boards. Add model number, either 7219-01 – First Place Steel (Level) Toe Board, 7219-02 – First Place Poly (Level) Toe Board, 7219-03- First Place Aluminum (Level) Toe Board, or 7219-04 – First Place Aluminum (Depressed) Toe Board.

Shot Put Toe Board:  Model No. ___ Shot Put Toe Board.

Specifier Notes: Remove the following line if specifying the 7219-01, 7219-02, or 7219-04 toe board.

- Toe Board: Constructed of cast aluminum with 1/4” wall thickness, 4” tall, and a white powder coat finish. To be mounted on a level throwing pad.

Specifier Notes: Remove the following line if specifying the 7219-01, 7219-02, or 7219-03 toe board.

- Toe Board: Constructed of cast aluminum with 1/2” wall thickness, 3 ¼” tall, and a white powder coat finish. To be mounted on a depressed throwing pad.

Specifier Notes: Remove the following line if specifying the 7219-02, 7219-03, or 7219-04 toe board.

- Toe Board: Constructed of 1/8” thick flat bar steel, 4” tall, and a white powder coat finish. To be mounted on a level throwing pad.

Specifier Notes: Remove the following line if specifying the 7219-01, 7219-03, or 7219-04 toe board.

- Toe Board: Fabricated from cross-link polyethylene with UV stabilizer, 4” tall, and a white finish. To be mounted on a level throwing pad.

E.	Take-Off Board Systems:

Specifier Notes: Specify the following paragraph for all take-off board systems. Add model number, either 7235-01 – First Place Championship Take-Off System or 7238-01 – First Place College/High School Take-Off System.

Take-Off Board System:  Model No. ___ Take-Off System.

Specifier Notes: Remove the following lines (1-5) if specifying the 7238-01 take-off system.

- Steel Tray:  Constructed of 13 gauge galvanized steel, formed and welded.

- Steel Underlay: Constructed of 13 gauge galvanized steel, welded together. Includes leveling bolts. The steel underlay can be adjusted for level and height, using six leveling bolts. The underlay has two holes for easy removal.

- Composite Take-Off Board: Constructed of ¾” Synthetic WPC (wood, plastic, composite), white in color. Comes already mounted to the steel underlay. The take-off board is reversible.  The board has two holes for easy removal.

- NCAA Foul Board: Constructed of ¾” Synthetic WPC (wood, plastic, composite), yellow in color. Comes already mounted to the steel underlay. The foul board is reversible.

- Steel Blanking Lid: Constructed of 13 gauge galvanized steel, welded together.  Includes leveling bolts.  The steel blanking lid can be adjusted for level and height using six leveling bolts. The lid has two holes for easy removal. Runway surface to be applied to the lid by the installer.

Specifier Notes: Remove the following lines (1-4) if specifying the 7235-01 take-off system.

- Steel Tray:  Constructed of 13 gauge galvanized steel, formed and welded.

- Steel Underlay: Constructed of 13 gauge galvanized steel, welded together. Includes leveling bolts. The steel underlay can be adjusted for level and height, using six leveling bolts. The underlay has two holes for easy removal.

- Composite Take-Off Board: Constructed of ¾” Synthetic WPC (wood, plastic, composite), white in color. Comes already mounted to the steel underlay. The take-off board is reversible.  The board has two holes for easy removal.

Specifier Notes: Remove the following line if not specifying the optional steel blanking lid.

- Optional Steel Blanking Lid: Constructed of 13 gauge galvanized steel, welded together.  Includes leveling bolts.  The steel blanking lid can be adjusted for level and height using six leveling bolts. The lid has two holes for easy removal. Runway surface to be applied to the lid by the installer.

F.	Pole Vault Boxes:

Specifier Notes: Specify the following paragraph for all pole vault boxes. Add model number, either 5831-01 – First Place Aluminum Vault Box, 5833-01 – First Place Cast Aluminum Vault Box, or 5830-01 – First Place Steel Vault Box

Pole Vault Box:  Model No. ___ Pole Vault Box.

Specifier Notes: Remove the following line if specifying the 5833-01 or 5830-01 pole vault box.

- Pole Vault Box: Constructed of 1/8” thick sheet aluminum formed with the back piece welded on. Two outside wings secure the vault box when cast in concrete.  The vault box has a white powder coat finish.

Specifier Notes: Remove the following line if specifying the 5831-01 or 5830-01 pole vault box.

- Pole Vault Box: Constructed of ½” thick aluminum cast into shape. Two outside wings secure the vault box when cast in concrete. The vault box has a white powder coat finish.

Specifier Notes: Remove the following line if specifying the 5833-01 or 5831-01 pole vault box.

- Pole Vault Box: Constructed of 12 gauge cold roll sheet steel formed with the back piece welded on. Two outside wings secure the vault box when cast in concrete. The vault box has a white powder coat finish.

Specifier Notes: Specify the following paragraph for all pole vault box lids. Remove the following section if not specifying vault box lids. Add model number, either 5831-02 – First Place Aluminum Vault Box Lid, 5833-02 – First Place Cast Aluminum Vault Box Lid, or 5830-02 – First Place Steel Vault Box Lid.

Pole Vault Box Lid: Model No. ___ Pole Vault Box Lid.

Specifier Notes: Remove the following line if specifying the 5833-02 or 5830-02 pole vault box lid.

- Pole Vault Box Lid: Constructed of 1/4” thick aluminum. 1½” welded steel tubes support the lid. The lid has a white powder coat finish.

Specifier Notes: Remove the following line if specifying the 5831-02 or 5830-02 pole vault box lid.

- Pole Vault Box Lid: Constructed of 8 gauge cold roll sheet steel. 1” x 1” welded steel tubes     support the lid. The lid has a black powder coat finish.

Specifier Notes: Remove the following line if specifying the 5831-02 or 5833-02 pole vault box lid.

3.	Pole Vault Box Lid: Constructed of 12 gauge steel plate. 1½” welded steel tubes support the lid.  The lid has a white powder coat finish.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive athletic field equipment.  Notify Architect in writing of conditions that would adversely affect installation or subsequent use.  Do not proceed with installation until unsatisfactory conditions are corrected.

3.2	INSTALLATION

A.	Install athletic field equipment in accordance with manufacturer's instructions and in compliance with local codes and regulations at locations indicated on the Drawings.

B.	Install equipment plumb, level, straight, square, accurately aligned, correctly located, to proper elevation, and secure.

C.	Install equipment using manufacturer's supplied hardware and fasteners.

D.	Repair minor damages to finish in accordance with manufacturer's instructions and as approved by Architect.

E.	Remove and replace damaged components that cannot be successfully repaired, as determined by Architect.

3.3	CLEANING

A.	Clean the athletic field equipment promptly after installation in accordance with manufacturer's instructions.

B.	Remove temporary protective coverings.

C.	Do not use harsh cleaning materials or methods that would damage finish.

D.	Do not remove warning labels and decals.

3.4	PROTECTION

A.	Protect installed items to ensure equipment will be without damage or deterioration at time of substantial completion.

END OF SECTION