M-F Athletic Company	May 2019

1600 Division Road

West Warwick, RI 02893

Toll Free		(800) 556-7464

Phone		(401) 942-9363

Fax		(800) 682-6950

Web Site		www.mfathletic.com

E-Mail		mfathletic@mfathletic.com

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the Drawings. Delete all “Specifier Notes” after editing this section. Section numbers are from MasterFormat 1995 Edition, with numbers from MasterFormat 2004 Edition in parentheses. Delete version not required.

SECTION 11480 (11 66 23.43) (11 68 33.43)

Discus Cages

Specifier Notes: This section includes all M-F Athletic Company, Inc. discus cages. Consult M-F Athletic Company, Inc. for assistance in editing this section for the specific application.

PART 1	GENERAL

  - SECTION INCLUDES

- Discus Cages

Specifier Notes: Remove the following line if not specifying the use of a barrier net.

- Barrier Nets

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. List other sections with work directly related to this section.

A.	Section 02200 (31 23 00) Excavation and Fill: Prepare site for the installation of in-ground equipment and back fill when installation is complete.

- Section 03300 (03 30 00) Cast-in-Place Concrete: Pouring of concrete under and around ground sleeves and surrounding areas.

C.	Section 02535 (32 18 23) Athletic Surfacing: Applying track surface material to the surrounding areas.

D. 	Section 02511 (32 12 16) Asphalt Paving: Applying asphalt sub-grade to the surrounding areas.

1.3	REFERENCES

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.4	DESIGN REQUIREMENTS

- Discus Cages: Locate positions and orientations of discus cages and their ground sleeves on the site plan.

1.5	SUBMITTALS

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including materials, components, fabrication, finish, and installation instructions.

C.	Operation and Maintenance Manual:  Submit manufacturer's operation and maintenance manual; including operation, maintenance, adjustment, and cleaning instructions; trouble shooting guide; parts list.

1.6	QUALITY ASSURANCE

A.	Single Source Responsibility:  Provide discus cages from single manufacturer.

B.	Manufacturer's Qualifications:  Minimum of 5 consecutive years experience manufacturing discus cages similar to that specified.

C.	Installer's Qualifications:  Contractor experienced with track & field installation, excavation, concrete work, asphalt paving, and track surfacing.

- Regulatory Requirements:  Discus cages shall conform to latest rules and regulations.

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.7	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.  Keep temporary protective coverings in place.

C.	Handling:  Protect materials and finish from damage during handling and installation.

1.8	WARRANTY

A.	Provide 1-year warranty against defects in materials and workmanship, unless otherwise specified.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	M-F Athletic Company, Inc., 1600 Division Road, West Warwick, Rhode Island, 02893.  Toll Free (800) 556-7464.  Phone (401) 942-9363.  Fax (800) 682-6950.  Web Site www.mfathletic.com.  E-Mail mfathletic@mfathletic.com.

Specifier Notes: Specify one of the following two paragraphs regarding substitutions. Edit as required for the project. Coordinate with Section 01630 (01 25 13) – Product Substitution Procedures.

B.	Substitutions:  Not permitted.

C.	Substitutions:  Requests for substitutions will be considered in accordance with Section 01630 (01 25 13).

2.2	DISCUS CAGES

Specifier Notes: Specify the following paragraph for all discus cages. Add model number, either 7257-01 – First Place Aluminum High School Discus Cage, 7259-01 – First Place Steel High School Discus Cage or 7266-01 – First Place Collegiate Discus Cage.

A.	Discus Cages:  Model No. ___ Discus Cage.

Specifier Notes: Remove the following line if specifying the 7259-01 or 7266-01 discus cage.

- Ground Sleeves: Consists of six (6) ground sleeves, constructed of aluminum, 28 1/4” long.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7266-01 discus cage.

- Ground Sleeves: Consists of six (6) ground sleeves, constructed of galvanized steel, 28 1/4” long.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7259-01 discus cage.

- Ground Sleeves: Consists of seven (7) ground sleeves, constructed of aluminum, 36” long.

Specifier Notes: Remove the following line if specifying the 7259-01 or 7266-01 discus cage.

- Net Poles: Consists of six (6) net poles, constructed of 2.875” aluminum pipe. The net poles will be off-set and stand at least 13’ tall when installed in the ground sleeves. The net poles will have rope tie-off cleats. The top of the net poles will be capped. The net poles will have eye bolts to hang the hoisting ropes from.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7266-01 discus cage.

- Net Poles: Consists of six (6) net poles, constructed of 2.375” galvanized steel pipe. The net poles will be off-set and stand at least 13’ tall when installed in the ground sleeves. The net poles will have rope tie-off cleats. The top of the net poles will be capped. The net poles will have eye bolts to hang the hoisting ropes from.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7259-01 discus cage.

- Net Poles: Consists of seven (7) net poles, constructed of 4” aluminum pipe. The net poles will be off-set and stand at least 16’7” tall when installed in the ground sleeves. The net poles will have rope tie-off cleats. The top of the net poles will be capped. The net poles will have pulleys to hang the hoisting ropes from.

- Hoisting Rope: The rope used to hang the net from the net poles will be 3/8” braided polyester, 20’ long. Each rope will have a net clip.

Specifier Notes: Remove the following line if specifying the 7266-01 discus cage.

- Net: Constructed of 100% white nylon 6 yarn solution dyed black, 1 7/8”sq mesh, raschel knotless netting, UV stabilizer added and heat-set, 340 lb break strength, rope bound, 13’ x 58’.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7259-01 discus cage.

- Net: Constructed of 100% white nylon 6 yarn solution dyed black, 1 7/8”sq mesh, raschel knotless netting, UV stabilizer added and heat-set, 340 lb break strength, rope bound, 17’ x 70’.

Specifier Notes: Remove the following line if specifying the 7266-01 discus cage.

- Tension Arms: Consists of six (6) tensions arms, 24” long.

Specifier Notes: Remove the following line if specifying the 7257-01 or 7259-01 discus cage.

- Tension Arms: Consists of seven (7) tensions arms, 30” long

- Warning Signs: Consists of three (3) warning signs constructed of polyethylene board 10” x 14”. The warning signs will be fastened to the outside of the net, at eye level, facing outward, at the front sides of the discus cage and at the rear of the discus cage.

- Barrier Nets:

Specifier Notes: Remove the following item if not specifying a barrier net. If specifying a barrier net add model number, either 7258-25 (works with 7257-01 and 7259-01 discus cage), or 7266-07 (works with 7266-01 discus cage).

Barrier Nets: Model No. ___ Barrier Net.

Specifier Notes: Remove the following line if specifying the 7266-07 barrier net.

- Barrier Net: Constructed of 100% white nylon 6 yarn solution dyed black, 1 7/8”sq mesh,               raschel knotless netting, UV stabilizer added and heat-set, 340 lb break strength, rope bound, 7’ x 63’.

Specifier Notes: Remove the following line if specifying the 7258-25 barrier net.

- Barrier Net: Constructed of 100% white nylon 6 yarn solution dyed black, 1 7/8”sq mesh,         raschel knotless netting, UV stabilizer added and heat-set, 340 lb break strength, rope bound, 7’ x 74’.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive discus cages.  Notify Architect in writing of conditions that would adversely affect installation or subsequent use.  Do not proceed with installation until unsatisfactory conditions are corrected.

3.2	INSTALLATION

A.	Install discus cages in accordance with manufacturer's instructions and in compliance with local codes and regulations at locations indicated on the Drawings.

B.	Install equipment plumb, level, straight, square, accurately aligned, correctly located, to proper elevation, and secure.

C.	Install equipment using manufacturer's supplied hardware and fasteners.

D.	Repair minor damages to finish in accordance with manufacturer's instructions and as approved by Architect.

- Remove and replace damaged components that cannot be successfully repaired, as determined by Architect.

3.3	CLEANING

A.	Clean the discus cages promptly after installation in accordance with manufacturer's instructions.

B.	Remove temporary protective coverings.

C.	Do not use harsh cleaning materials or methods that would damage finish.

D.	Do not remove warning labels and decals.

3.4	PROTECTION

A.	Protect installed discus cages to ensure equipment will be without damage or deterioration at time of substantial completion.

END OF SECTION