M-F Athletic Company	May 2019

1600 Division Road

West Warwick, RI 02893

Toll Free		(800) 556-7464

Phone		(401) 942-9363

Fax		(800) 682-6950

Web Site		www.mfathletic.com

E-Mail		mfathletic@mfathletic.com

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the Drawings. Delete all “Specifier Notes” after editing this section. Section numbers are from MasterFormat 1995 Edition, with numbers from MasterFormat 2004 Edition in parentheses. Delete version not required.

SECTION 11480 (11 66 23.43) (11 68 33.43)

Pole Vault Boxes

Specifier Notes: This section M-F Athletic Company, Inc. pole vault boxes. Consult M-F Athletic Company, Inc. for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

- Pole Vault Boxes

- Pole Vault Box Lids

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. List other sections with work directly related to this section.

A.	Section 02200 (31 23 00) Excavation and Fill: Prepare site for the installation of in-ground equipment and back fill when installation is complete.

B.	Section 03300 (03 30 00) Cast-in-Place Concrete: Pouring of concrete under and around pole vault boxes.

C.	Section 02535 (32 18 23) Athletic Surfacing: Applying runway material up to the edges of the pole vault box.

D. 	Section 02511 (32 12 16) Asphalt Paving: Applying asphalt sub-grade to run way.

1.3	REFERENCES

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.4	DESIGN REQUIREMENTS

A.	Pole vault boxes:  Locate positions of pole vault boxes on the site plan.

1.5	SUBMITTALS

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including materials, components, fabrication, finish, and installation instructions.

C.	Operation and Maintenance Manual:  Submit manufacturer's operation and maintenance manual; including operation, maintenance, adjustment, and cleaning instructions; trouble shooting guide; parts list.

1.6	QUALITY ASSURANCE

A.	Single Source Responsibility:  Provide pole vault boxes from single manufacturer.

B.	Manufacturer's Qualifications:  Minimum of 5 consecutive years experience manufacturing pole vault boxes similar to that specified.

C.	Installer's Qualifications:  Contractor experienced with track & field installation, concrete work, asphalt paving, and track surfacing.

D.	Regulatory Requirements:  Pole vault boxes shall conform to latest rules and regulations.

Specifier Notes: Specify the applicable associations. Association rule books are updated each year around September 1.

1.	National Federation of State High School Associations (NFHS).

2.	National Collegiate Athletic Association (NCAA)

3.	International Association of Athletics Federations (IAAF)

1.7	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.  Keep temporary protective coverings in place.

C.	Handling:  Protect materials and finish from damage during handling and installation.

1.8	WARRANTY

A.	Provide 1-year warranty against defects in materials and workmanship, unless otherwise specified.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	M-F Athletic Company, Inc., 1600 Division Road, West Warwick, Rhode Island, 02893.  Toll Free (800) 556-7464.  Phone (401) 942-9363.  Fax (800) 682-6950.  Web Site www.mfathletic.com.  E-Mail mfathletic@mfathletic.com.

Specifier Notes: Specify one of the following two paragraphs regarding substitutions. Edit as required for the project. Coordinate with Section 01630 (01 25 13) – Product Substitution Procedures.

B.	Substitutions:  Not permitted.

C.	Substitutions:  Requests for substitutions will be considered in accordance with Section 01630 (01 25 13).

2.2	POLE VAULT BOXES

Specifier Notes: Specify the following paragraph for all pole vault boxes. Add model number, either 5831-01 – First Place Aluminum Vault Box, 5833-01 – First Place Cast Aluminum Vault Box, or 5830-01 – First Place Steel Vault Box

A.	Pole Vault Box:  Model No. ___ Pole Vault Box.

Specifier Notes: Remove the following line if specifying the 5833-01 or 5830-01 pole vault box.

1.	Pole Vault Box: Constructed of 1/8” thick sheet aluminum formed with the back piece welded on. Two outside wings secure the vault box when cast in concrete.  The vault box has a white powder coat finish.

Specifier Notes: Remove the following line if specifying the 5831-01 or 5830-01 pole vault box.

2.	Pole Vault Box: Constructed of ½” thick aluminum cast into shape. Two outside wings secure the vault box when cast in concrete. The vault box has a white powder coat finish.

Specifier Notes: Remove the following line if specifying the 5833-01 or 5831-01 pole vault box.

3.	Pole Vault Box: Constructed of 12 gauge cold roll sheet steel formed with the back piece welded on. Two outside wings secure the vault box when cast in concrete. The vault box has a white powder coat finish.

Specifier Notes: Specify the following paragraph for all pole vault box lids. Remove the following section if not specifying vault box lids. Add model number, either 5831-02 – First Place Aluminum Vault Box Lid, 5833-02 – First Place Cast Aluminum Vault Box Lid, or 5830-02– First Place Steel Vault Box Lid.

B.	Pole Vault Box Lid: Model No. ___ Pole Vault Box Lid.

Specifier Notes: Remove the following line if specifying the 5833-02 or 5830-02 pole vault box lid.

- Pole Vault Box Lid: Constructed of 1/4” thick aluminum. 1½” welded steel tubes support the lid. The lid has a white powder coat finish.

Specifier Notes: Remove the following line if specifying the 5831-02 or 5830-02 pole vault box lid.

2.	Pole Vault Box Lid: Constructed of 8 gauge cold roll sheet steel.	1” x 1” welded steel tubes           support the lid. The lid has a black powder coat finish.

Specifier Notes: Remove the following line if specifying the 5831-02 or 5833-02 pole vault box lid.

3.	Pole Vault Box Lid: Constructed of 12 gauge steel plate. 1½” welded steel tubes support the lid.  The lid has a white powder coat finish.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive pole vault boxes.  Notify Architect in writing of conditions that would adversely affect installation or subsequent use.  Do not proceed with installation until unsatisfactory conditions are corrected.

3.2	INSTALLATION

A.	Install pole vault boxes in accordance with manufacturer's instructions at locations indicated on the Drawings.

B.	Install equipment plumb, level, straight, square, accurately aligned, correctly located, to proper elevation, and secure.

C.	Install equipment using manufacturer's supplied hardware and fasteners.

D.	Repair minor damages to finish in accordance with manufacturer's instructions and as approved by Architect.

E.	Remove and replace damaged components that cannot be successfully repaired, as determined by Architect.

3.3	CLEANING

A.	Clean pole vault boxes promptly after installation in accordance with manufacturer's instructions.

B.	Remove temporary protective coverings.

C.	Do not use harsh cleaning materials or methods that would damage finish.

D.	Do not remove warning labels and decals.

3.4	PROTECTION

A.	Protect installed pole vault boxes to ensure equipment will be without damage or deterioration at time of substantial completion.

END OF SECTION