M-F Athletic Company	May 2019

1600 Division Road

West Warwick, RI 02893

Toll Free		(800) 556-7464

Phone		(401) 942-9363

Fax		(800) 682-6950

Web Site		www.mfathletic.com

E-Mail		mfathletic@mfathletic.com

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the Drawings. Delete all “Specifier Notes” after editing this section. Section numbers are from MasterFormat 1995 Edition, with numbers from MasterFormat 2004 Edition in parentheses. Delete version not required.

SECTION 11480 (11 66 23.43) (11 68 33.43)

Shot Put/Hammer and Discus Circles

Specifier Notes: This section includes all M-F Athletic Company, Inc. shot put/hammer and discus circles. Consult M-F Athletic Company, Inc. for assistance in editing this section for the specific application.

PART 1	GENERAL

  - SECTION INCLUDES

- Shot Put/Hammer Circles

- Discus Circles

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. List other sections with work directly related to this section.

A.	Section 02200 (31 23 00) Excavation and Fill: Prepare site for the installation of in-ground equipment and back fill when installation is complete.

- Section 03300 (03 30 00) Cast-in-Place Concrete: Pouring of concrete under and around shot put/hammer and discus circles and surrounding areas.

C.	Section 02535 (32 18 23) Athletic Surfacing: Applying track surface material to the surrounding areas.

D. 	Section 02511 (32 12 16) Asphalt Paving: Applying asphalt sub-grade to the surrounding areas.

1.3	REFERENCES

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.4	DESIGN REQUIREMENTS

- Sot put/hammer and discus circles: Locate positions and orientations of shot put/hammer and discus circles and related fixtures on the site plan.

1.5	SUBMITTALS

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including materials, components, fabrication, finish, and installation instructions.

C.	Operation and Maintenance Manual:  Submit manufacturer's operation and maintenance manual; including operation, maintenance, adjustment, and cleaning instructions; trouble shooting guide; parts list.

1.6	QUALITY ASSURANCE

A.	Single Source Responsibility:  Provide all shot put/hammer and discus circles from single manufacturer.

B.	Manufacturer's Qualifications:  Minimum of 5 consecutive years experience manufacturing shot put/hammer and discus circles similar to that specified.

C.	Installer's Qualifications:  Contractor experienced with track & field installation, excavation, concrete work, asphalt paving, and track surfacing.

- Regulatory Requirements:  Shot put/hammer and discus circles shall conform to latest rules and regulations.

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.7	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.  Keep temporary protective coverings in place.

C.	Handling:  Protect materials and finish from damage during handling and installation.

1.8	WARRANTY

A.	Provide 1-year warranty against defects in materials and workmanship, unless otherwise specified.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	M-F Athletic Company, Inc., 1600 Division Road, West Warwick, Rhode Island, 02893.  Toll Free (800) 556-7464.  Phone (401) 942-9363.  Fax (800) 682-6950.  Web Site www.mfathletic.com.  E-Mail mfathletic@mfathletic.com.

Specifier Notes: Specify one of the following two paragraphs regarding substitutions. Edit as required for the project. Coordinate with Section 01630 (01 25 13) – Product Substitution Procedures.

B.	Substitutions:  Not permitted.

C.	Substitutions:  Requests for substitutions will be considered in accordance with Section 01630 (01 25 13).

2.2	ATHLETIC FIELD EQUIPMENT

A.	Shot Put/Hammer Circles:

Specifier Notes: Specify the following paragraph for all shot put/hammer circles. Add model number, either 7216-02 – First Place Web Shot/Hammer Circle or 7218-02 – First Place Aluminum Shot and Hammer Circle.

Shot Put/Hammer Circles:  Model No. ___ Shot Put/Hammer Circle.

Specifier Notes: Remove the following line if specifying the 7218-02 shot put/hammer circle.

- Circle: Consists of two halves of a circle constructed of 2 ¾” x 1/4” galvanized steel, with 1” x 1” galvanized steel angle cross-bracing. The circle shall be cast in concrete so that the throwing surface is depressed 3/4”. The circle shall have a 7' diameter.

Specifier Notes: Remove the following line if specifying the 7216-02 shot put/hammer circle.

- Circle: Consists of 1” x 3/4” x 1/4” aluminum angle that is roll bent to 42” (106.7cm) radius. Four arcs form the circle.  The circle can be cast in concrete so that the throwing surface is depressed 3/4” or installed directly on top of the concrete pad. The circle shall have a 7' diameter.

- Discus Circles:

Specifier Notes: Specify the following paragraph for all discus circles. Add model number, either 7216-01 – First Place Web Discus Circle or 7218-01 – First Place Aluminum Discus Circle.

Discus Circles:  Model No. ___ Discus Circle.

Specifier Notes: Remove the following line if specifying the 7218-01 discus circle.

- Circle: Consists of two halves of a circle constructed of 2 ¾” x 1/4” galvanized steel, with 1” x 1” galvanized steel angle cross-bracing. The circle shall be cast in concrete so that the throwing surface is depressed 3/4”. The circle shall have an 8'-2 1/2” diameter.

Specifier Notes: Remove the following line if specifying the 7216-01 discus circle.

- Circle: Consists of 1” x 3/4” x 1/4” aluminum angle that is roll bent to 49 7/32” (125.0 cm) radius. Four arcs form the circle.  The circle can be cast in concrete so that the throwing surface is depressed 3/4” or installed directly on top of the concrete pad. The circle shall have an 8'-2 1/2” diameter.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive shot put/hammer and discus circles.  Notify Architect in writing of conditions that would adversely affect installation or subsequent use.  Do not proceed with installation until unsatisfactory conditions are corrected.

3.2	INSTALLATION

A.	Install shot put/hammer and discus circles in accordance with manufacturer's instructions and in compliance with local codes and regulations at locations indicated on the Drawings.

B.	Install equipment plumb, level, straight, square, accurately aligned, correctly located, to proper elevation, and secure.

C.	Install equipment using manufacturer's supplied hardware and fasteners.

D.	Repair minor damages to finish in accordance with manufacturer's instructions and as approved by Architect.

E.	Remove and replace damaged components that cannot be successfully repaired, as determined by Architect.

3.3	CLEANING

A.	Clean the shot put/hammer and discus circles promptly after installation in accordance with manufacturer's instructions.

B.	Remove temporary protective coverings.

C.	Do not use harsh cleaning materials or methods that would damage finish.

D.	Do not remove warning labels and decals.

3.4	PROTECTION

A.	Protect installed shot put/hammer and discus circles to ensure equipment will be without damage or deterioration at time of substantial completion.

END OF SECTION