M-F Athletic Company	May 2019

1600 Division Road

West Warwick, RI 02893

Toll Free		(800) 556-7464

Phone		(401) 942-9363

Fax		(800) 682-6950

Web Site		www.mfathletic.com

E-Mail		mfathletic@mfathletic.com

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the Drawings. Delete all “Specifier Notes” after editing this section. Section numbers are from MasterFormat 1995 Edition, with numbers from MasterFormat 2004 Edition in parentheses. Delete version not required.

SECTION 11480 (11 66 23.43) (11 68 33.43)

Shot Put Toe Boards

Specifier Notes: This section includes all M-F Athletic Company, Inc. shot put toe boards. Consult M-F Athletic Company, Inc. for assistance in editing this section for the specific application.

PART 1	GENERAL

  - SECTION INCLUDES

- Shot Put Toe Boards

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. List other sections with work directly related to this section.

A.	Section 02200 (31 23 00) Excavation and Fill: Prepare site for the installation of in-ground equipment and back fill when installation is complete.

- Section 03300 (03 30 00) Cast-in-Place Concrete: Pouring of concrete under and around shot put toe boards and surrounding areas.

C.	Section 02535 (32 18 23) Athletic Surfacing: Applying track surface material to the surrounding areas.

D. 	Section 02511 (32 12 16) Asphalt Paving: Applying asphalt sub-grade to the surrounding areas.

1.3	REFERENCES

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.4	DESIGN REQUIREMENTS

- Shot Put Toe Boards: Locate positions and orientations of shot put toe boards on the site plan.

1.5	SUBMITTALS

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including materials, components, fabrication, finish, and installation instructions.

C.	Operation and Maintenance Manual:  Submit manufacturer's operation and maintenance manual; including operation, maintenance, adjustment, and cleaning instructions; trouble shooting guide; parts list.

1.6	QUALITY ASSURANCE

A.	Single Source Responsibility:  Provide all shot put toe boards from single manufacturer.

B.	Manufacturer's Qualifications:  Minimum of 5 consecutive years experience manufacturing shot put toe boards similar to that specified.

C.	Installer's Qualifications:  Contractor experienced with track & field installation, excavation, concrete work, asphalt paving, and track surfacing.

- Regulatory Requirements:  Shot put toe boards shall conform to latest rules and regulations.

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.7	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.  Keep temporary protective coverings in place.

C.	Handling:  Protect materials and finish from damage during handling and installation.

1.8	WARRANTY

A.	Provide 1-year warranty against defects in materials and workmanship, unless otherwise specified.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	M-F Athletic Company, Inc., 1600 Division Road, West Warwick, Rhode Island, 02893.  Toll Free (800) 556-7464.  Phone (401) 942-9363.  Fax (800) 682-6950.  Web Site www.mfathletic.com.  E-Mail mfathletic@mfathletic.com.

Specifier Notes: Specify one of the following two paragraphs regarding substitutions. Edit as required for the project. Coordinate with Section 01630 (01 25 13) – Product Substitution Procedures.

B.	Substitutions:  Not permitted.

C.	Substitutions:  Requests for substitutions will be considered in accordance with Section 01630 (01 25 13).

2.2	SHOT PUT TOE BOARDS

A.	Shot Put Toe Boards:

Specifier Notes: Specify the following paragraph for all shot put toe boards. Add model number, either 7219-01 – First Place Steel (Level) Toe Board, 7219-02 – First Place Poly (Level) Toe Board, 7219-03- First Place Aluminum (Level) Toe Board, or 7219-04 – First Place Aluminum (Depressed) Toe Board.

Shot Put Toe Board:  Model No. ___ Shot Put Toe Board.

Specifier Notes: Remove the following line if specifying the 7219-01, 7219-02, or 7219-04 toe board.

- Toe Board: Constructed of cast aluminum with 1/4” wall thickness, 4” tall, and a white powder coat finish. To be mounted on a level throwing pad.

Specifier Notes: Remove the following line if specifying the 7219-01, 7219-02, or 7219-03 toe board.

- Toe Board: Constructed of cast aluminum with 1/2” wall thickness, 3 ¼” tall, and a white powder coat finish. To be mounted on a depressed throwing pad.

Specifier Notes: Remove the following line if specifying the 7219-02, 7219-03, or 7219-04 toe board.

- Toe Board: Constructed of 1/8” thick flat bar steel, 4” tall, and a white powder coat finish. To be mounted on a level throwing pad.

Specifier Notes: Remove the following line if specifying the 7219-01, 7219-03, or 7219-04 toe board.

- Toe Board: Fabricated from cross-link polyethylene with UV stabilizer, 4” tall, and a white finish. To be mounted on a level throwing pad.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive shot put toe boards.  Notify Architect in writing of conditions that would adversely affect installation or subsequent use.  Do not proceed with installation until unsatisfactory conditions are corrected.

3.2	INSTALLATION

A.	Install shot put toe boards in accordance with manufacturer's instructions and in compliance with local codes and regulations at locations indicated on the Drawings.

B.	Install equipment plumb, level, straight, square, accurately aligned, correctly located, to proper elevation, and secure.

C.	Install equipment using manufacturer's supplied hardware and fasteners.

D.	Repair minor damages to finish in accordance with manufacturer's instructions and as approved by Architect.

E.	Remove and replace damaged components that cannot be successfully repaired, as determined by Architect.

3.3	CLEANING

A.	Clean the shot put toe boards promptly after installation in accordance with manufacturer's instructions.

B.	Remove temporary protective coverings.

C.	Do not use harsh cleaning materials or methods that would damage finish.

D.	Do not remove warning labels and decals.

3.4	PROTECTION

A.	Protect installed shot put toe boards to ensure equipment will be without damage or deterioration at time of substantial completion.

END OF SECTION