M-F Athletic Company	May 2019

1600 Division Road

West Warwick, RI 02893

Toll Free		(800) 556-7464

Phone		(401) 942-9363

Fax		(800) 682-6950

Web Site		www.mfathletic.com

E-Mail		mfathletic@mfathletic.com

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the Drawings. Delete all “Specifier Notes” after editing this section. Section numbers are from MasterFormat 1995 Edition, with numbers from MasterFormat 2004 Edition in parentheses. Delete version not required.

SECTION 11480 (11 66 23.43) (11 68 33.43)

Take-Off Board Systems

Specifier Notes: This section includes all M-F Athletic Company, Inc. take-off board systems. Consult M-F Athletic Company, Inc. for assistance in editing this section for the specific application.

PART 1	GENERAL

  - SECTION INCLUDES

- Take-Off Board Systems

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. List other sections with work directly related to this section.

A.	Section 02200 (31 23 00) Excavation and Fill: Prepare site for the installation of in-ground equipment and back fill when installation is complete.

- Section 03300 (03 30 00) Cast-in-Place Concrete: Pouring of concrete under and around take-off board systems and surrounding areas.

C.	Section 02535 (32 18 23) Athletic Surfacing: Applying track surface material up to the edges of the take-off board systems and on steel blanking lid if used.

D. 	Section 02511 (32 12 16) Asphalt Paving: Applying asphalt sub-grade to the runway.

1.3	REFERENCES

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.4	DESIGN REQUIREMENTS

- Take-off Board Systems: Locate positions and orientations of take-off board systems on the site plan.

1.5	SUBMITTALS

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including materials, components, fabrication, finish, and installation instructions.

C.	Operation and Maintenance Manual:  Submit manufacturer's operation and maintenance manual; including operation, maintenance, adjustment, and cleaning instructions; trouble shooting guide; parts list.

1.6	QUALITY ASSURANCE

A.	Single Source Responsibility:  Provide take-off board systems from single manufacturer.

B.	Manufacturer's Qualifications:  Minimum of 5 consecutive years experience manufacturing take-off board systems similar to that specified.

C.	Installer's Qualifications:  Contractor experienced with track & field installation, excavation, concrete work, asphalt paving, and track surfacing.

- Regulatory Requirements:  Take-off board systems shall conform to latest rules and regulations.

Specifier Notes: List standards referenced in this section, complete with designations and titles. Delete standards not referenced. This article does not require compliance with standards, but is merely a listing of those used.

- NFHS – National Federation of State High School Associations (NFHS)

- NCAA – National Collegiate Athletic Association (NCAA)

- IAAF – International Association of Athletics Federations (IAAF)

1.7	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.  Keep temporary protective coverings in place.

C.	Handling:  Protect materials and finish from damage during handling and installation.

1.8	WARRANTY

A.	Provide 1-year warranty against defects in materials and workmanship, unless otherwise specified.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	M-F Athletic Company, Inc., 1600 Division Road, West Warwick, Rhode Island, 02893.  Toll Free (800) 556-7464.  Phone (401) 942-9363.  Fax (800) 682-6950.  Web Site www.mfathletic.com.  E-Mail mfathletic@mfathletic.com.

Specifier Notes: Specify one of the following two paragraphs regarding substitutions. Edit as required for the project. Coordinate with Section 01630 (01 25 13) – Product Substitution Procedures.

B.	Substitutions:  Not permitted.

C.	Substitutions:  Requests for substitutions will be considered in accordance with Section 01630 (01 25 13).

2.2	TAKE-OFF BOARD SYSTEMS

A.	Take-Off Board Systems:

Specifier Notes: Specify the following paragraph for all take-off board systems. Add model number, either 7235-01 – First Place Championship Take-Off System or 7238-01 – First Place College/High School Take-Off System.

Take-Off Board System:  Model No. ___ Take-Off System.

Specifier Notes: Remove the following lines (1-5) if specifying the 7238-01 take-off system.

- Steel Tray:  Constructed of 13 gauge galvanized steel, formed and welded.

- Steel Underlay: Constructed of 13 gauge galvanized steel, welded together. Includes leveling bolts. The steel underlay can be adjusted for level and height, using six leveling bolts. The underlay has two holes for easy removal.

- Composite Take-Off Board: Constructed of ¾” Synthetic WPC (wood, plastic, composite), white in color. Comes already mounted to the steel underlay. The take-off board is reversible.  The board has two holes for easy removal.

- NCAA Foul Board: Constructed of ¾” Synthetic WPC (wood, plastic, composite), yellow in color. Comes already mounted to the steel underlay. The foul board is reversible.

- Steel Blanking Lid: Constructed of 13 gauge galvanized steel, welded together.  Includes leveling bolts.  The steel blanking lid can be adjusted for level and height using six leveling bolts. The lid has two holes for easy removal. Runway surface to be applied to the lid by the installer.

Specifier Notes: Remove the following lines (1-4) if specifying the 7235-01 take-off system.

- Steel Tray:  Constructed of 13 gauge galvanized steel, formed and welded.

- Steel Underlay: Constructed of 13 gauge galvanized steel, welded together. Includes leveling bolts. The steel underlay can be adjusted for level and height, using six leveling bolts. The underlay has two holes for easy removal.

- Composite Take-Off Board: Constructed of ¾” Synthetic WPC (wood, plastic, composite), white in color. Comes already mounted to the steel underlay. The take-off board is reversible.  The board has two holes for easy removal.

Specifier Notes: Remove the following line if not specifying the optional steel blanking lid.

- Optional Steel Blanking Lid: Constructed of 13 gauge galvanized steel, welded together.  Includes leveling bolts.  The steel blanking lid can be adjusted for level and height using six leveling bolts. The lid has two holes for easy removal. Runway surface to be applied to the lid by the installer.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive take-off board systems. Notify Architect in writing of conditions that would adversely affect installation or subsequent use.  Do not proceed with installation until unsatisfactory conditions are corrected.

3.2	INSTALLATION

A.	Install take-off board systems in accordance with manufacturer's instructions and in compliance with local codes and regulations at locations indicated on the Drawings.

B.	Install equipment plumb, level, straight, square, accurately aligned, correctly located, to proper elevation, and secure.

C.	Install equipment using manufacturer's supplied hardware and fasteners.

D.	Repair minor damages to finish in accordance with manufacturer's instructions and as approved by Architect.

E.	Remove and replace damaged components that cannot be successfully repaired, as determined by Architect.

3.3	CLEANING

A.	Clean the take-off board systems promptly after installation in accordance with manufacturer's instructions.

B.	Remove temporary protective coverings.

C.	Do not use harsh cleaning materials or methods that would damage finish.

D.	Do not remove warning labels and decals.

3.4	PROTECTION

A.	Protect take-off board systems to ensure equipment will be without damage or deterioration at time of substantial completion.

END OF SECTION